## Slide 1: Externally Mounted Composite Radome / Fairings for Special Mission Applications
FAA Workshop on Modifications and Alterations affecting Composite Parts or Composite Structure
July 19-20, 2016

## Slide 3: Gulfstream Special Mission Experience

## Slide 4: Gulfstream Special Mission Experience
GI
TC-4C A-6 Trainer
GII/GIIB
NASA Shuttle Trainer
US Military Research Testbed

## Slide 5
GIII
  Foreign Military Cargo Door Installation
GIV / G450
  US Military Cargo Door Installation
  Foreign Military Signal Intelligence
  Gov VIP Transport
Gulfstream Special Mission Experience

## Slide 6: Gulfstream’s Experience - Special Missions
GV / G550
  Foreign Military Signal Intelligence
  Foreign Military Tracking / Surveillance
  Domestic / Foreign Atmospheric Research Platforms
  Gov VIP Transport

## Slide 7: Gulfstream’s Experience – Special Missions
Types of Special Mission Modifications / Installations
Nose Radome
Forward Fuselage Belly Radome (Canoe)
Forward Fuselage Upper Fairings
Forward Fuselage Side Fairings
Aft Fuselage Lower Fairing
Empennage Tip Cap Radome
Tailcone / Ventral Fin
Wing Stores

## Slide 8: Gulfstream’s Experience – Special Missions
Each Modification has its own unique design challenges
All radome / fairing modifications require composite material of some type
  Transmissivity
  Weight
  Stiffness
  Complex Contours

## Slide 9: Gulfstream’s Experience – Special Missions
Most Challenging are Fuselage Belly Radomes or ‘Canoes’
  Largest
  Most Complex due to -
    Mission / Customer Requirements
    Aircraft Requirements
    Regulatory Requirements

## Slide 10: Radome Structural Design Criteria
Customer Driven Requirements
  Transmissivity
  Field of View
  Maintenance Access
Aircraft Driven Requirements
  Aerodynamic Loading
    Flight Envelope / Mission Profile
  Structural Loading
    Airframe Deflection
      Forced Deflection

## Slide 11: Radome Structural Design Criteria
Selected Regulatory Requirements
Design and Construction
  25.601 General
  25.603 Materials
  25.605 Fabrication Methods
  25.609 Protection of Structure
  25.613 Material Strength Properties and Material Design Values
Structure
  25.301 Loads
  25.303 Factor of Safety
  25.305 Strength and Deformation
  25.307 Proof of Structure

## Slide 12: Radome Structural Design Criteria
Selected Regulatory Requirements
Structure - Continued
25.365(e) Pressurized Compartment Loads
25.571 Damage Tolerance
    Fatigue Assessement
    Parts Departing Aircraft
    Birdstrike – section 25.571(e)(1)
25.581 Direct Effects of Lightning

## Slide 13: Radome Structural Design Criteria
Policy Statement
  PS-ACE100-2004-10030 Substantiation of Secondary Composite Structures
  PS-ANM-25-17 Structural Certification Criteria for Antennas, Radomes, and Other External Modifications
Advisory Material
  AC 20-107B Composite Aircraft Structure

## Slide 14: Radome Structural Design Criteria
Company / Customer Criteria
Structures not tested to ultimate loads should maintain min. M.S. = 0.25
  If tested, min would be M.S.= 0.00
  Ref. MIL-HDBK-516C
Aero Pressure loads to have ultimate load factor of 2.0
  May reduce to 1.5 based on previous tests
Belly pod sizing based on external pressure loads and inertia loading
  Inertia to include emergency landing and flight inertial

## Slide 15: 25.603 Material 25.613 Material Design Values
Material
  Typically fiberglass or quartz fiber
    Required for transmissivity characteristics
    Graphite/Epoxy for non transmission locations

## Slide 16: 25.603 Material 25.613 Material Design Values
Previous Programs
  Fiberglass material used throughout components
    Other radomes / fairings
    Material testing implemented to validate material data
      Strength
      Modulus
      Strain Cutoffs
      Critical Environmental Conditions

## Slide 17: 25.603 Material 25.613 Material Design Values
Current / Future Programs
  More sophisticated equipment requiring more advanced material
    Testing programs developed to generate next generation of design values
    Material Equivalency testing to existing material databases
    Extensive use of NIAR facilites/capabilities

## Slide 18: 25.605 Fabrication
Radome / Canoe Fabrication
Panels / Shell
  Solid Laminate or Honeycomb Sandwich
  Mission Dependent
Fabrication Processes
  Well Understood
    Neither new nor novel
  In house fabrication process specifications
  Previously approved

## Slide 19: 25.305 Proof of Structure 25.307 Strength and Deformation
  Both classical analysis and FEM are employed.
  Laminates are analyzed by typical laminate sizing routines
    Strain cutoffs
    Buckling criteria
  FEM Model validation
    Unit loading / classical solutions
    Constraints Checks
    Deflection Checks
    Boundary Conditions

## Slide 20: 25.305 Proof of Structure 25.307 Strength and Deformation
  Maintain minimum M.S. for untested structure
    Customer / company requirement
  Testing performed to validate analysis and analytical details
    Fuselage Proof Pressure
    Attachment fittings

## Slide 21: 25.365(e) – Pressurized Compartment Loads
Belly pods are not pressurized but are attached to pressurized fuselage
Requirement per 25.365(e) requires any structure outside a pressurized compartment to be able to withstand the sudden release of pressure from fuselage
Belly pods designs incorporate means of venting the radome in a fuselage decompression event.

## Slide 22: 25.571 Damage Tolerance
Fatigue Assessment
  Influence of Canoe / Belly Pod Radome on aircraft fatigue life is addressed
  Affected sections of airframe are reviewed and updated if required
Parts Departing Aircraft
  Fuselage Canoe / Belly pod radomes
    All designs have multiple attachments at frame locations
    Design incorporates ability to lose connections
    ‘Get Home’ loading

## Slide 23: 25.571 Damage Tolerance
Inspections are established
  Radome laminate
  Fittings attaching radome to fuselage
  Impact damage of composite shell

## Slide 24: 25.571(e) - Birdstrike
Previous Programs
Birdstrike testing performed
Bird will penetrate radome
  Bird disintegrates on impact
    Composite fiber toughness
    shreds the bird
  No parts separated from test article
Assessment of penetration
  Ram air effect due to hole
  Full aerodynamic pressurization
  Multiple fitting design

## Slide 25: 25.581 – Direct Effects of Lightning
Belly Pod Radomes are generally located in primary strike zone locations
Segmented diverters are typically utilized
  Leading edges/extremities
  Mesh in acreage not in FOV
Testing
  High voltage determines attachment location
  High current validates protection strategy

## Slide 26: Summary
Composite Belly Pod / Canoe Radome designs have been in service on Gulfstream aircraft for over 25 years
Fiberglass / Graphite Composite material utilized throughout all designs
Successful Implementation based on
  Conservative design criteria
  Sound material selection
  Proven fabrication methods
  Reliable structural analysis techniques
  Systematic inspection

## Slide 27: Questions?