## Slide 1: Repair and Modification of Primary Composite Structural Components – Substantiation Complexities for Non-OEMs Within the Scope of both Field Approvals and STC Projects
Stephen Forness
Managing Director –
Air Flight Technical LLC

## Slide 2: Where Would Someone Start
Complexity of the Problem
  Antenna vs Major PSE(s) Modification
  STC vs Field Approval
Design, Manufacturing, Quality Assurance
Material Properties
Structural Substantiation (Static, Fatigue, and
Damage Tolerance)

## Slide 3: Original Manufacture Information
Ply Layup
Material(s) Used
OEM material properties used in original design. (Including all building block test)
OEM BVID Results used in Damage Tolerance Design
Design Loads – External
Design Loads - Internal
Defects covered by OEM MRB and allowed to remain that can affect the repair or modification

## Slide 4: What Will Be Needed
STC
Process Specifications
Material Qualification
Inspection Methods
C-Scan
A-Scan (What limitations does this cause)
Detail Part Manufacturing
Curing Methods (Autoclave, Oven-
Vacuum, and Room Temperature)
Trimming
Field Approval – All process Specification on Drawings

## Slide 5: Material Properties
Equivalence (70 K $) – Basic OEM Laminate
Complete Basic Material Properties (CMH-17
Data Set) (150 K $)
Building Block Approach for Each Modification Or Repair (25-150 K $)
MRB (e.g. property reduction due to
porosity)

## Slide 6: Process Specifications
Assembly Processes
Bonding
Drilling
Priming
Painting
Decal Application
etc.

## Slide 7: Design
Details Needed on Drawings
Ply Flat Patterns
Finish Article Ply Location
Assemblies / Installations
Inspection prior to modification
Callout of all appropriate Process
Specification

## Slide 8: Quality Assurance
Inspection Requirements – Detail Parts, Assembly, Installations
Inspection Methods – C-Scan, A-Scan, etc.
MRB Manual / Procedures

## Slide 9: Inspection Used – Before and After
Need to first assess the existing structural integrity,
  C-Scan or A-Scan
Second to ensure quality of the repair or modification
  C-Scan or A-Scan

## Slide 10: Design Issues
Location Selection
  Minimize complexity as much as possible
Less is more – Minimize effect on existing Load
Path
Clearly present work plan for correct installation (Utilize SRM Methods and procedures as much as possible)
Replace Lightning protection

## Slide 11: Structural Substantiation
FEM (Load Distribution Only)
Bi-axial loads needed (not just hoop)
Close Form Solutions
Details analysis
Failure Criteria
Bonded Joint analysis
Bearing / Bi-Pass Curves based on
different layups
Damage Tolerance Substantiation

## Slide 13: Effects of Defects Before and After
Effects on properties of porosity, voids and other manufacturing defects
Effects on properties of damage (Impact, Heat Damage etc)

## Slide 14: Plan Differences between STC and Field Approvals
Material Properties
Inspection Techniques – Before and After
Design Issues
Analysis Methodologies
Effects of Defects Before and After
Process Specification for Bonding, Drilling, etc.
Experience of the Installation Mechanics

## Slide 15: Possible Analysis Criteria Pyramid - Fuselage
Bolted Analysis – Bolt Loads / Bearing Bypass
Bonding Analysis (Peel /
Maximum Shear)
FEM – Validation (Load
Distribution Only)
Bird Strike (Analysis
and Test)

## Slide 16: Possible Analysis Criteria Pyramid - Empennage
Flutter / Stiffness
Bonding Analysis (Peel /
Maximum Shear)
Aerodynamic
Smoothness
Weight / Re-Balance

## Slide 17: Conclusion
Repairs and modification of primary aircraft structures will be performed without OEM assistance!!!