## Slide 1: Perspectives on Modifications and Alterations on Modern Composite Airplanes
Paul Brey
July 20, 2016
FAA Workshop on Modifications and Alterations Affecting Composite Parts or Composite Structures

## Slide 2: Starting Point
AC43-214, Repairs and Alterations to Composite and Bonded Aircraft Structure
Key: The standard for alterations and modifications is exactly the same as for initial type certification
Notes: This is difficult for new entrants and inexperienced modifiers to understand.
Many want to commercialize modifications the same way they would do for themselves.

## Slide 3: Required Data for FAA Approval or Acceptance
Per AC43-214
  Drawings
  Substantiation Data
  Material Specifications
  Fabrication and Process Specifications
  Inspection Procedures
  Defect Accept/Reject Criteria
Nothing new here.

## Slide 4: Comparison to Conventional Metal Structure
Conventional metal structure has a deep body of knowledge and experience to guide engineering design and substantiation of most design changes
Composites are less clear

## Slide 5: Metal Structures
AC 43.13-2 guidance
Evolution of fail safe, fatigue, damage tolerant design, and finally, understanding the combination of these results in current regulation
Regulations end up requiring test based evidence to address damage tolerance and wide spread fatigue damage

## Slide 6: Metal Structures
How can non-DAH entities address need for test?
AFS-300 Major Repair/Alteration Data Approval Job Guide provides experience based guidance!

## Slide 7: Metal Structures

## Slide 8: Metal Structures

## Slide 10: Metal Structures

## Slide 11: Metal Structures
Accepted and proven methods and material properties
  MMPDS
  NASGRO SW
  AFGROW SW
  Robust FEA
Simple isotropic materials with recognized spec basis
Conventional, time proven design configurations
Well established NDI methods

## Slide 12: What Do We Have For Composite Structures?
It took more than a half century to develop experience, guidance, and methods to manage fabric, wood, and aluminum structures
Few composite materials are stable in production for more than a decade
  Material producers are continuously improving mechanical performance or processing ease/cost
  OEMs and new entrants constantly seek advantage

## Slide 13: Composite Structures
How will industry and regulatory entities monitor aging performance?
How will we “normalize” this information to allow combining information to generalize conclusions about materials and configurations?

## Slide 14: Alterations and Modifications – Why?
Changes, Alterations, and Modifications a natural part of the life and safety improvement progression of a new system entering operations!

## Slide 15: Life Cycle Progression for a New System

## Slide 16: Life Cycle Progression for a New System

## Slide 17: Life Cycle Progression for a New System

## Slide 18: Life Cycle Progression for a New System

## Slide 19: Life Cycle Progression for a New System

## Slide 20: Life Cycle Progression for a New System

## Slide 21: Alterations and Modifications - Why
Aging Systems will always need improvements to compete with newer systems
Operational economics drives this need

## Slide 22: What Should We Expect?
Correction or enhancement to address initial design shortfalls
Performance Enhancement
  Re-engine
  Drag Reduction
  Fuel Quantity Increase
  Weight Growth

## Slide 23: What Should We Expect?
Systems and Safety Upgrades
  Avionics and Flight Controls improvements
    Instruments/Displays
    Sensors
    Autopilot/Servos
    Autoland/Autonomous Flight
  Comm and Operational Environment
    ADS-B
    RVSM
    Next Next Gen?
These will be the most common changes in the future: Antennas and new equipment installations

## Slide 24: What Should We Expect?
Systems and Safety Upgrades
  Known Ice capability
  Condition Monitoring
Condition Monitoring may offer the greatest long term safety benefit to manage systems and structures

## Slide 25: What Should We Expect?
Passenger Amenities
  Environmental Comfort
  Interiors
  Passenger Communication Systems/Internet
We should be expecting a sudden proliferation of modifications to add high band width internet

## Slide 26: DAH vs Other Engineering Entity
We have to accept that the DAH has the advantage
  Material data
  Configuration data
  Loads
  Validated models
  Test data
  Knowledge of margins
DAH generally wants to keep this advantage

## Slide 27: DAH vs Other Engineering Entity
Other Engineering Entities still need to meet the same standard
  More work!
  More investment!
  Or, smart partnering arrangements…
There is no substitute for a real, marketable alteration with a viable business plan
As an engineering service provider, you should confirm this before taking projects
Notes: There really is no substitute for a real, marketable alteration with a viable business plan.
Too bad the FAA can’t reject projects with little or no value

## Slide 28: Designing Alterations
Purpose of Alteration
Clearly describe the intent and impact of the modification
  Why are you doing the modification?
  What flight and ground conditions are affected?
  How is aircraft performance affected?
  What systems are affected?
  What load paths are affected?
  What are the critical environmental considerations?
  Conduct a thorough FMEA

## Slide 29: Designing Alterations
Major vs Minor
  This is a crucial determination
  Policy guidance on Substantiation of Secondary Composite Structures, PS-ACE100-2004-10300 is very helpful
  Introducing new materials into an airframe will still need specification and test support
  Test for credit means “major” or STC, coordinate certification plans early

## Slide 30: Designing Alterations
Material Considerations and Selection
  Foundation for the design
  Assess structural and system impact for selected material
  Available Data:
    With few exceptions, supplier data is of little value
    What else is out there?
      DAH AMM/SRM information
      ARP information
      CMH17/AGATE
      Development of proprietary data

## Slide 31: Designing Alterations
Material Considerations and Selection
How much testing at the material level?
  Select materials with existing allowable if possible!

## Slide 32: Designing Alterations
What is the strategy for ensuring part and installation integrity?
  Substantiate and control materials and process for repeated application
  Or
  Substantiate individual fabrication and installation instances
This selection determines the level of conservatism of the analytical and test substantiation

## Slide 33: Designing Alterations
Substantiate and control materials and process for repeated application
Material and process spec required
Allowables or equivalency per guidance
Select properties important to specific details of design
  Include properties that will need RI inspection and that the material supplier can provide
Include bond and co-bond allowables for lap joints and design detail specific joints

## Slide 34: Designing Alterations
Substantiate individual fabrication and installation instances
Allowables or equivalency testing per existing guidance to assess local variability
Selection of instance based witness coupon testing for critical properties in substantiation
Test procedures and commercial arrangement for instance based testing
Use of very conservative allowables to reduce risk of failure of witness coupons
Substantiation analysis and/or testing of substandard instance of installation or component

## Slide 35: Design and Substantiation
Reference AC20-107
Loads
  DAH sources
  Estimation
  Local testing and reverse engineering
Static strength – conventional and FEA techniques tailored to allowables

## Slide 36: Design and Substantiation
Plan for Continued Airworthiness
  This is the backbone for safe continued operation!
  Robust field inspection plan is the best insurance for continued airworthiness
  Probability of Detection matters – it should be proven for the defects that will be allowed
  Selection of allowed defects determine both static and DT substantiation rigor

## Slide 37: Design and Substantiation
Damage Tolerance
  My experience is based in testing with defects
  In most cases, element level testing can be sufficient for component and relatively small modifications
    In well analyzed structure, there is usually one or several critical details that drive or bound overall performance
  Larger modification may need full scale test
  What is the state of art for analytical substantiation?

## Slide 38: Inspection
Development of appropriate inspection method and standard to bound lower level of acceptance
At the part or component fabrication level, and the installation

## Slide 39: Evolution of Policy - Comments
Composite airframes, as we know them today, will be more costly to develop and substantiate alterations for non-DAH’s than metal structures – this needs to be communicated to less inexperienced applicants
It would seem that use of composites will generally reduce or eliminate the economic advantage of modification as a means to move aircraft from one intended operational use to another alternate use such as freight or air ambulance, as has been practice with metal airplanes

## Slide 40: Evolution of Policy - Comments
This is counter to the likely outcome that composite airplanes may have very long extended life durability compared to metal construction

## Slide 41: Evolution of Policy - Comments
We don’t know the aging response to composite aircraft construction yet
  Conservative design criteria have generally resulted in no-growth DT designs; so we don’t really know the damage tolerance, life, or fatigue wear out margins we are dealing with
  Initial indications tell us conservative design criteria result in little or no structural decay, at least not in any measurable or conclusively inspectable way
  Bond joint, bolt joints, and metal fittings will likely be the culprit.
For sure, as substantiated life is approached, there will be demand by owner/operator to extend them

## Slide 42: Evolution of Policy - Comments
As an industry, we need to develop new bodies of knowledge and new approaches to developing alterations

## Slide 43: Questions I Have
Are non-DAH alterations really needed to continue proliferation of system and operational safety improvement?
What is the role of structural health and condition monitoring in the future?
  Can operational oversight compensate for less long term experience with an equivalent level of safety?
Can we develop an infrastructure to support “instance based” material and process verification?
Notes: It will take a lot of resources to develop non-DAH methods and data

## Slide 44: Thank You For Listening!
Question?